## Slide 1
Dave Strenski
March 2023
Learning about solar power, the life and death of an electron.
He was always
so negative
Baby Minus

## Slide 2
Slide 2
2006
2007
2008
2009
2010
2011
2012
2013
2014
2015
2016
SolarYpsi History
Win $6k grant
4 panels on Co-op
Start solar talks
Concentrate video
City Hall solar fund raise $1050
City Hall solar idea meet with the Mayor
Win City Hall,
Co-op grant $36k
Win Bakery solar grant $44.6k
Grow Co-op system
SEIA video
Adams School $12k
Google video, crash website
iTunesU video
TEDx video
EnvMich Report
1000 roof resolution
$93.6k donation for six non-profits
HomePower Mag.
Michigan Clean Energy Report
SolarYpsi website by Nik Estep
Solar power Heritage Festival
Chasing Clean Air, CA radio podcast
QR tags
Cameron solar videos
$25k for Fire Station
NPR State Side
Partner Chart House Energy
Highland Cemetery
Letters to neighbors
2005
$10k for solar talks

## Slide 3
Slide 3
2017
2018
SolarYpsi History
FireHouse Mag.
SolarToday Mag.
HomePower Mag.
DoE SunShot
Shining City top 20
50 Big roofs
Scan all of Ypsilanti
2019
2020
2021
Fire Station expansion
DPS expansion
Parkridge DoE proj.
17 res. solar projects
3 Solar Moonshot projects, $75k
First solar car port
7 Solar Moonshot projects, $175k
Solar for City pool, $25k
Cem&Crem Mag.

## Slide 4
KWH
Sunny
Boy
325
KWH
KWH
Forward
Meter
Reverse
Meter
Gen Meter
sun
2005
2005
2005
2005
2007
2008
2008
2008
2008
2008
2008
2008
100
9885
534
327
store meters
disconnect
inverter
photovoltaic panels
breaker panel
utility meters

## Slide 6
Steeper for more uniform annual power
Flatter for maximum annual power
Tracking systems
Seasonal fixed panels
Fixed panels

## Slide 7
Silicon [Si]
+
n
14 neutrons
14 protons
shell 1
shell 2
shell 3
valence electrons

## Slide 8
Silicon [Si]
+
n
14 neutrons
14 protons
shell 1
shell 2
shell 3
valence electrons

## Slide 9
wires on the top
wires on the bottom
silicon doped with boron
(holes, few less electrons)
silicon doped with phosphorus
(few extra electrons)
Building a Solar Cell

## Slide 10
holes migrate down
electrons
migrate up
photons

## Slide 11
Mono and Polycrystalline Silicon
60 cell
72 cell
40” x 79”
450-watts
66”tall
380W
split-cell
Tesla
Uni-Solar
Amorphous Silicon
Uni-Solar
PowerHome

## Slide 12
KWH
Sunny
Boy
325
KWH
KWH
Forward
Meter
Reverse
Meter
Gen Meter
sun
2005
2005
2005
2005
2007
2008
2008
2008
2008
2008
2008
2008
100
9885
534
327
store meters
disconnect
inverter
photovoltaic panels
breaker panel
utility meters

## Slide 13
UL listed
Clean power
Shuts offs if grid is down
Powered by solar
Quite and Cool
Displays power generated
DC in
AC out
time
voltage
AC
voltage
DC
time

## Slide 14
Standard breaker
240 volt, 20 amp
back fed

## Slide 15
4:00 am
OFF
forwards

## Slide 16
8:00 am
direct
current
alternating
current
forwards

## Slide 17
11:00 am
direct
current
alternating
current
forwards

## Slide 18
1:00 pm
direct
current
alternating
current
backwards

## Slide 19
Utility supplies power to the transmission lines
Power is distributed to the neighborhood
Solar panels start generating power

## Slide 20
Utility supplies power to the transmission lines
Power is distributed to the neighborhood
Solar panels start generating power
One less shovelful of coal is needed at the utility power plant

## Slide 22
Solar Economics
Average Michigan home
668 kWh/month (average month)
18.11c per kWh, $121/month (2023)
668 kWh / 30 days = 22 kWh (average day)
https://www.michigan.gov/-/media/Project/Websites/mpsc/consumer/electric/rates1.pdf?rev=959038e92dbd465a9293dd7152009d4f

## Slide 24
Solar Economics
4 hour of sun per day, assuming panels are facing south tilted at your latitude.
Assume 20% loss for system efficiency and some shading
22 kWh / 4 hr * 1.2 = 6.6 KW
6600 watts would be about 16 solar panels at 410W per panel. (2 x 8 array, 13’ x 27’)
Average Michigan home
668 kWh/month (average month)
18.11c per kWh, $121/month (2023)
668 kWh / 30 days = 22 kWh (average day)

## Slide 27
Solar installation cost = $3.0 per watt $3.5 per watt
6600W x $3/W = $19,800 6600W x $3.5/W = $23,100
$19,800 x 0.30 = -$5,940 $23,100 x 0.30 = -$6,930
$13,860 $16,170
6.6 kW x 4 hr x $0.1811 = $4.78/day
$4.78 x 365 days = $1,745/year
@ $3.0/watt $13,860 / $1,745 = ~8 years ROI
@ $3.5/watt $16,170 / $1,745 = ~9 years ROI
City of Ypsilanti
@ $3.0/watt ($13,860-$2000) / $1,745 = ~7 years
@ $3.5/watt ($16,170-$2000) / $1,745 = ~8 years
Solar Economics
4 hour of sun per day, assuming panels are facing south tilted at your latitude.
Assume 20% loss for system efficiency and some shading
22 kWh / 4 hr * 1.2 = 6.6 kW
6600 watts would be about 16 solar panels at 410W per panel. (2 x 8 array, 13’ x 27’)
Average Michigan home
668 kWh/month (average month)
18.11c per kWh, $121/month (2023)
668 kWh / 30 days = 22 kWh (day)

## Slide 28
Solar Economics

## Slide 29
Intel 80486 PC
Purchased in 1990 for $2000
16 MB of Memory, 50 MHz clock
50 pounds and BIG.
Samsung Galaxy Nexus
2013 for $200
32 GB , 1.2 GHz clock, dual-core
5 ounces and fits in your pocket
23 years = 10x cheaper, 2000x memory, 48x faster, 160x lighter
Economics of Scale

## Slide 30
21% useful
79% lost
65% lost
35% useful
4% solar
9% wind